## Slide 1: Module: CPU Activity Briefing
2110221 Computer Engineering Essential

## Slide 2: Brookshere’s Simple Machine
16 general-purpose registers ($0 - $F)
Program Counter ($PC)
Instruction Register ($IR)
256 bytes main memory (@00 - @FF)
Control Unit
Register Unit
$0
A3
$1
0A
$F
…
Main Memory
@00
11
@01
0A
@02
22
@03
01
@FE
27
@FF
BA
BUS
ALU
PC
02
IR
110A
https://www.amazon.com/Computer-Science-Overview-Glenn-Brookshear/dp/0133760065
@04
51
@05
12
$2
00

## Slide 3: Machine Cycle: Fetch-Decode-Execute
Fetch
Decode
Execute
1. Retrieve the next instruction from memory (as indicated by the program counter) to the instruction register and then increment the program counter
2. Decode the bit pattern in the instruction register
3. Perform the action required by the instruction in the instruction register

## Slide 4: Parts of Instruction
Op-code (Operation code) – 4 bits
  Specify the operation to execute
Operand – 12 bits
  Additional details about operation
    Address, register, constant
0101
0001
0001
0010
Op-code
Operand
5
1
1
2
ADD
[RST] -- R = S + T
r1 <- r1 + r2

## Slide 7: Part-1 Decoding Instructions

## Slide 8: Part-2 Playing with Emulator

## Slide 9: Part-3 Writing Programs

## Slide 10: Part-3 Outstanding